## Slide 1: Maze Navigation Using LiDAR Scans
Maor Amitai, Yair Vax
Project presentation · August 2026

## Slide 2: The Task and the Approach
The task
Navigate a robot through a two-dimensional maze from point A to point B — without ever being told its own position or the position of the goal.
The approach
Replace explicit (x,y) coordinates with sequences of LiDAR readings. A diffusion model plans directly in scan space; a localizer converts scans back into positions only for control.
Why it is hard
Giant mazes are made of long, self-similar corridors, so many different places produce almost identical scans. The core difficulty is ambiguity, not control.
Constraint: the planner never sees x or y, in any form, at any point — every position it acts on is inferred from the sensor.

## Slide 3: Technical Architecture
STAGE 1
Diffusion planner
Generates a trajectory of future LiDAR scans from a start scan and a goal scan.
STAGE 2
Executor
inverse-dynamics model mapping current scan → desired scan into joint torques.
Environment: OGBench AntMaze Giant, then PointMaze Giant Stitch. Everything runs on comp_diffuser_release.

## Slide 4: Project Timeline
Kickoff
Navigate a 2-D maze from A to B with (x,y) input.
LiDAR port
Lidar scans replace (x,y). simulated laser, dataset conversion, retrained diffusion and inverse dynamics.
Localization
3-D pose grid (x, y, θ), likelihood maps, candidate ranking.
Ant improvements and plateau
End-to-end tops out near 10%. Goal-scan ambiguity, not control, is the binding constraint.
Pivot to the ball + keep improving ant.
Verify and hop, improving ant movment, fixing goal localization.
Ball: Viterbi + budget
Viterbi decode lifts @1000 from 19.0 to 45.2. Step budget corrected to OGBench's 1000.

## Slide 5: The First Result After the LiDAR Port: 0%
The first end-to-end run on AntMaze Giant with (x,y) replaced by LiDAR scans reached the goal in none of the episodes
0%
Success rate after the port
AntMaze Giant · scans in place of coordinates
WHAT WAS ALREADY WORKING
Dataset conversion, simulated laser, retrained diffusion planner and inverse dynamics — the pipeline ran end to end.
WHAT WE DID NOT YET KNOW
Why it was zero. Perception, control and goal ambiguity were all still stacked on top of each other.

## Slide 6: First Problem: The Ant Would Not Move
The inverse dynamics model never saw the ant's joint angles — restoring them lifted action-prediction R² from 0.26 to 0.88
THE PROBLEM
The inverse dynamics model was missing the joint angles of the ant's legs. The robot did not move at all.
THE SOLUTION
Reconstruct the missing joint angles and feed them in as part of the input vector to the model.
THE RESULT
The robot actuated — the ant starts walking. First purposeful motion in the environment.
0.26
R² before the fix
Poor prediction of the required actions
0.88
R² after the fix
Dramatic improvement in action prediction

## Slide 7: The Central Problem: Goal Ambiguity
LOW UNIQUENESS
One scan is not an address
In a maze of long, self-similar corridors, a single LiDAR scan taken from the goal cell is not unique. different cells produce an almost identical scan.
SIGNAL, NOT SKILL
The ability is there
when the top-scoring plan happens to sit in the right cell, routing is correct. It just is not reliable.
Diagnosis: the bottleneck is the representation of the goal and the movement of the ant, not the planner's capacity to produce a route.

## Slide 8: Goal Ambiguity Visualization

## Slide 9: Attempted Fix: Multi-Scan Goal
Replace the single goal scan with a short approach sequence — retraining succeeded, the maze still did not get solved
THE IDEA
Replace the single goal scan with a short sequence of K scans taken as the agent approaches the goal.
THEORETICAL ADVANTAGE
The approach sequence encodes spatial context — which should have resolved the goal-representation ambiguity.
THE ACTUAL RESULT
Retraining went through successfully, but the robot still failed to solve the maze.

## Slide 10: First Success!
A 3-D (x, y, θ) localization grid over the maze led to the first end-to-end success
WHAT MADE IT WORK
We built a 3-D grid over (x, y, θ): one copy of the map per heading, stored as rows × columns × orientations. Headings sit about 30° apart to match the scan data, and the grid resolution keeps a run to a few minutes.
0% → ~10%
End-to-end success rate, AntMaze Giant

## Slide 11: Lifting The Success Rate
Change | What it did | Result
Verify and hop | Use the ranked candidate list as a fallback plan instead of committing to one guess. | 2 / 20
Scanning every 10° | 36 orientation bins instead of 12, to recognise the goal cell more often. | Worse — 65% of true cells missed the list entirely
Better ant movement | When the ant is stuck in place, head for the most open direction and replan. | 4 / 20 — slight improvement
Fixed goal-cell localization | Deduce the goal cell from 12 scans at the true goal and compare it against every other cell (MSE-like), instead of from an approach sequence. | 50% with orientation, 39% without
Less replanning | Replan only when needed, instead of unconditionally every 500 steps. | 46% — slightly worse; 4,500 → 4,000 steps
Target: lift the success rate from 10% toward the 60% of the original (x,y) diffuser
Net effect: the goal-cell fix carried almost all of the gain — 10% to ≈39%/50%; every other knob was flat or negative.

## Slide 12: Candidate List After Fixed goal-cell Localization

## Slide 13: Ant Aftermath
SECTION 02
Ant aftermath

## Slide 14: Example of a few runs
aliasing
In this batch of runs, most of the time the first contender was aliased to a different similar cell.
- the first contender

## Slide 15: Aliasing Map

## Slide 16: The Ball
PointMaze giant-stitch — a point mass that navigates from 30 range beams alone
SECTION 03
True-LiDAR on the ball

## Slide 17: Why We Moved to the Ball
THE REASON
The ant plateaued
End-to-end success topped out near 10%, with three failure sources stacked on top of each other: control, self-localization and goal ambiguity.
WHAT IT REMOVES
No heading, no learned executor
A point mass has no orientation, so scans are a pure function of position and the reference grid drops from 12 angular bins to 1. OGBench drives it with a proven P-law.
WHAT SURVIVES
Goal-scan aliasing
The one hard problem is unchanged: different places still produce near-identical scans. That is geometry, not agent — and it is the science we wanted to study.
Both perception channels now measure free. Reading LiDAR instead of the state costs nothing measurable; the whole remaining gap is planner and executor.

## Slide 18: The Pipeline
01
Sensor
A 30-beam scan, full 2π field of view, 12 wu max range, raycast against the true maze map. Yaw is identically zero.
02
Planner
Composed diffusion in 30-D scan space. 8 segments × 160 frames, overlap 56, giving an 888-frame scan plan. Start and goal scans inpainted.
03
Decode
A Viterbi localizer over a grid of 4,409 poses. Max-product over whole paths turns the scan plan into (x,y) carrot targets.
04
Pursuit
BFS waypoints plus a cursor: an argmin over a 61-index forward window, 2 wu of plan arc ahead, line-of-sight checked.
05
Executor
PID with Kp = 5, bit-identical to upstream's proven P-law. Saturated on roughly 90% of steps.
Belief runs alongside. A sequence-consistent grid filter localizes the ball every step from its live scan, seeded from the start scan; the same likelihood machinery localizes the goal scan.

## Slide 19: The Viterbi Decode: Most Impactful Improvement
Max-product over paths replaced per-step argmax in the plan decode — zero retraining, CPU-only, +26 pts @1000 steps
THE FAULT
The filter decode took the argmax independently at every step, so it emitted carrot targets the ball physically could not follow. 89% of the steps where the ball came off its plan sat on one — 8% null, lift 10.6x, p = 1.7e-137.
THE FIX
Max-product over paths on the 4,409-pose grid (0.5 wu lattice). It removes 100% of the infeasible carrots and lowers the scan-match residual — the model's scans were always better explained by a continuous path.
19.0 → 45.2
@1000 steps · +26.2 pts
p = 1.2e-24 — the headline number
57.0 → 77.6
@2500 steps · +20.6 pts
p = 6.2e-20 — historical budget

## Slide 20: Where We Stand
500 episodes per arm (5 tasks × 20 problems × 5 seeds). Success latches, so budget buys score.
45.2 ± 0.8
Ours @1000 steps
Viterbi, 5 seeds × 100 problems
68 ± 3
CompDiffuser (paper)
(x,y) obs + learned inverse dynamics
−22.8 pts
Gap to close
~29 pts of it is recoverable time

## Slide 21: The Eval Ladder Is Flat
Rung | Goal comes from | Position from | Isolates | @2500, 3 seeds
L1 | True goal scan | True (x,y) | Planner + decode quality | 55.0 ± 6.6
L2 | Likelihood-decoded goal cell | True (x,y) | Goal localization | 55.0 ± 5.3
L3 — the deliverable | Decoded goal cell | Belief filter | Self-localization (full True-LiDAR) | 57.0 ± 5.0
L4 | Both modes | Both | Planner-free BFS ceiling | 0% (last-mile, stale)
Each rung adds exactly one error source — so we can price each one separately
Both perception steps are free. Goal localization: 165 vs 165, p = 1.0, with 55/100 episodes bit-identical. Self-localization: 171 vs 165, p = 0.57, median error 0.260 wu on a 0.5 wu lattice.

## Slide 22: Half the Budget Produces No Motion
Where the first 1,000 steps go | Share | Counterfactual @1000
Moving — always at max speed (0.200 / 0.283 wu) | 49.3% | —
A-idle — frozen, carrot sitting on the ball | 17.7% | 51.4
B-pinned — frozen, carrot far, PID saturated | 32.9% | 64.2
Both removed — same plans, model and decode | 50.7% | 74.2
51% of the first 1,000 control steps move the ball zero world units — there is no “slow”, only stopped or at max speed
A is pursuit geometry, not visibility. 57% of idle steps had a visible point within 2 wu of plan arc and idled anyway.
A tangent almost always exists. 85% of pinned steps have a free beam ≥1 wu wide still pointing goal-ward.

## Slide 23: New Approch: Frequent Replanning With History Taken Into Account
The decoder matches each scan to the grid on its own, so every new plan is decoded without the ball's history
HOW THE DECODER WORKS
A memoryless argmin: for each scan it picks the grid point whose reference scan is most similar, with no link to previous frames.
WHAT HAPPENS ON REPLAN
The ball gets teleported. Each fresh plan is decoded from scratch, with nothing tying it to where the ball has just been.
OUR ASSESSMENT
History is the missing input. We tried several workarounds; feeding history in is hard because the decoder we chose cannot use it. We see this as a future direction.

## Slide 24: Summary
WHAT WE TRIED
Plan in scan space
We replaced (x,y) with LiDAR scans: a diffusion planner generates a trajectory of scans, and a localizer decodes it back into positions the agent can follow.
ANT · ANTMAZE GIANT
0% → ≈39–50%
Restoring joint angles, a 3-D (x, y, θ) pose grid and a goal-cell fix took the ant from 0% to its best result. Goal-scan aliasing set the ceiling.
BALL · POINTMAZE GIANT
45.2% @1000 steps
The Viterbi decode lifted success from 19.0% to 45.2% (77.6% @2500), against 68% for CompDiffuser with (x,y) input.

## Slide 25: Additional Things We Can Try
1 · CHEAPEST
Finish the frozen-time arms
Arms 2 and 3 are shipped but unrun. Screen one seed per arm, read the mechanism gate before the score, then 5 seeds on any winner. Ceiling +19.0 pts.
2 · STRUCTURAL
Rewrite the pursuit fixed point
The cursor only advances when the ball moves. Advance on plan index against elapsed time, or project the ball onto the plan polyline. ~40 lines plus one screening job.
3 · OWED
Re-run the offline suite
Every G2a/G2b number was computed with the decode we later proved was emitting teleports. CPU-only, existing dumps — tells us whether “the planner is incoherent” is still true.
4 · THE SCIENCE
Attack the planner residual
Blocks 0 and 1 hold plans that genuinely go elsewhere; no timing fix touches them. Replan cadence first, then the one sensing lever still live for block 1.